## Slide 1: PDEs and Characteristics Governing Dynamical Systems: Optimal-Harvesting Path Planning and Lagrangian Analysis of Inertial Particles
Manan Doshi
Advisor: Prof. Pierre Lermusiaux

## Slide 2: Background and Motivation
Predicting the transport of inertial and dynamically active particles in the ocean is essential for the health of our planet.
Marine Plastic Pollution
The Ocean Cleanup
Deep sea mining plumes
Marcel Petroleum Exploration
Plankton and biomass transport
NASA Earth Observatory
Peacock et al., Physics Today ‘13
Oil spills
Sargassum Invasion
Mexico News Daily
Examples include:
Notes: These are complex phenomenon that we’d like to be able to predict so as to understand their ecological impacts on the ocean

## Slide 3: Background and Motivation
Examples of problems we aim to solve:
Time-optimal collection of a field of marine material
Time-optimal path planning for dynamically-constrained vehicles that can collect energy from their surroundings
The Ocean Cleanup
NOAA
The optimal collection and monitoring of active materials is also essential for the efficient protection and sustainable utilization of the ocean.
The Ocean Cleanup
3
Saildrone
Liquid Robotics
Liquid Robotics

## Slide 4: Underlying Idea
State augmentation to create a higher-dimensional PDE whose characteristics are the governing equations of our dynamical system.
Recall: method of characteristics
Predicting transport of passive particles using flow maps
Time-optimal path planning in dynamical flows
Predicting transport of inertial/dynamically active particles using flow maps
Time-optimal path planning in dynamical flows with dynamic collection constraints
Existing methods
Derived methods
4
Notes: - Better graphic for characteristic

## Slide 5: Optimal-Harvesting Path Planning
Goal: Find the quickest path for a vehicle:
From start point to destination
In a flow in which the vehicle is being advected
Which is dynamic
While collecting a required amount of background field
Which is also dynamic!
We base our method on the algorithm developed for time-optimal path planning using the Level Set method4.
State of the art
  Based on:
  Rapidly exploring random trees1
  A* search2
  Artificial potential methods3
sub-optimal, heuristic dependent, for static fields
Issues:
We build upon methods for time-optimal path planning
1 Kuffner, ICRA ’01; 2 Garau, ICRA ’05; 3 Warren, AUV ’90; 4 Lolla et al., ICRA ’12; Lolla et al. Ocean Dynamics ’14
5
Notes: TODO: Rearrange or whitespace: CK

## Slide 6
Lolla et al., ICRA ’12; Lolla et al. Ocean Dynamics ’14; Lolla & Lermusiaux SICON ’17; Lermusiaux et al., HOE ’13
  Start
  End
  Start:
  End:
Exact, Time-Optimal Path Planning with Level Sets
  How to evolve the reachability front?
  Reachability front
  Contour containing the set of positions that can be reached at a given time
  Implicitly represented as the zero level set of a signed distance function
  Lagrangian viewpoint
  Eulerian viewpoint
  Backtrack optimal trajectory once destination is reached
6
Notes: TODO: Arrangement

## Slide 7
Attract level set to locations with high values of field
Heuristic, sub-optimal, parameter-dependent, may not provide a solution.
Energy-optimal path planning:
  Tracks energy for the ‘vehicles’ of interest on the reachability front; then stop vehicles that run out of energy
  Incorrect; possible to collect more by staying inside the front.
  Can be solved using stochastic optimization1 when no energy is harvested ( )
  Expensive, relies on reduced order representations of F(t), not generalizable.
Optimal-Harvesting Path Planning
1: Subramani, Deepak N., and Pierre FJ Lermusiaux, Ocean Modelling 100 (2016): 57-77.
How do we integrate field collection into our framework?
7
Start
Destination
Harvesting dynamics
Background flow
Max vehicle speed
Vehicle heading
Vehicle dynamics

## Slide 8
Optimal-Harvesting Path Planning
Solution: State-space augmentation to obtain a higher-dimensional Hamilton-Jacobi equation
Characteristics include collection dynamics and vehicle dynamics
8
Notes: Needs some illustrations. Break into 2 slides. Make big D into small d

## Slide 9
Special Case 1: Optimal-Collection Path Planning
Hamilton-Jacobi equation for reachability front evolution
Maximization
TVD - RK4
5th-order WENO
Godunov Method
9

## Slide 10: Example 1: Optimal-Collection Path Planning
Start point
Final point
Collection constraint: 0.8
Max Speed: 0.4
10

## Slide 11
Example 1: Optimal-Collection Path Planning
Start point
Final point
Collection constraint: 0.8
Max Speed: 0.4
Notes: TODO: 2 videos

## Slide 12: Example 1: Optimal-Collection Path Planning
Backtrack to obtain the optimal path
Solution features:
Velocity field used to reach destination quickly
Vehicle collected requisite amount of field
12
Time Optimal Path
Collection Constrained Path
Notes: `

## Slide 13: Example 2: Optimal-Collection Validation
To validate that our solver indeed gives us the optimal path, we test it on a case where we have manufactured an analytical solution
13

## Slide 14: Example 2: Optimal-Collection Validation
14

## Slide 15: Example 2: Optimal-Collection Validation
15

## Slide 16
Special Case 2: Energy-Optimal Path Planning
Hamilton-Jacobi equation for reachability front evolution
Maximization
16
Notes: Big D to small d

## Slide 17
Example 3: Energy-Optimal Path Planning
17
Start point
Final point
Starting Energy: 0.5
K : 40
Max speed: 0.2
Notes: Note: update with fine case

## Slide 18
Example 3: Energy-Optimal Path Planning
18
Notes: Note: update with fine case

## Slide 19
Example 3: Energy-Optimal Path Planning
19

## Slide 20
Example 3: Energy-Optimal Path Planning
20

## Slide 21: Lagrangian Analysis of Inertial Particles
Existing approach: Assume passive particles;
compute flow map;
Forward flow map: Where do particles go?
Backward flow map: Where do particles come from?
Governing ODE for passive particles
Computing the flow map
Run trajectories on a grid of particles to get their final positions
Advection of initial position gives us the backward flow map1
Goal: To collect a field of particles, we need to be able to predict how the particles move.
1: Kulkarni, Chinmay, and Lermusiaux, Pierre JCP 2019
Marine Plastic Pollution
The Ocean Cleanup
Plankton and biomass transport
NASA Earth Observatory
Sargassum Invasion
Mexico News Daily
21
Forward and Backward PDE advections of positions
Feppon and Lermusiaux, SIAM Review ’18
Notes: Outline before jump

## Slide 22: Lagrangian Analysis of Inertial Particles
How do we integrate inertial particles into this methodology?
Governing ODE for inertial particles:
simplified Maxey-Riley equation
Forward flow map
Backward flow map
Flow map is a mapping between initial and final positions
Flow map is a mapping between initial and final positions states
Goal: Given a fluid flow, predict the transport of inertial particles.
22
Force by undisturbed flow
Buoyancy
Stokes drag
Added mass
Basset-Boussinesq memory term

## Slide 23: Lagrangian Analysis of Inertial Particles
Governing PDE for the flow map: analogous to that of passive particles
23
Dynamics for passive particles
Augmented state dynamics, inertial particles
Augmented PDE
PDE for computing flow maps
TVD - RK4 with composition
WENO
Notes: Write the full MR eqn with explanation for each term

## Slide 24
Example: Inertial Particles
  Example: Analytical Double Gyre
  X and Y flow maps at
  Red: Inertial particle Blue: Passive particle
  Compute state-augmented flow maps for inertial particles by considering an augmented state space of particle position and velocity, i.e. , its acceleration is:
  Evolve according to the PDE:
Notes: Density of water: 1000
Density of particles: 1200
Viscosity (nu): 1e-6
Particle size: 1e-3
The flow maps are now 4D (function of x, y, V_x, V_y), so we plot a 2D cross section at V_x = 0 and V_y = 0
That is, these are the final positions of the particles that started at the corresponding x, y locations with zero initial velocity
The white spaces start appearing because particles that started at those locations leave the domain (even though it is a closed domain, inertial particles can leave as they can have enough inertia)
The left two trajectories are extracted from the flow map on the right (which implicitly solves for all trajectories).
The interesting case is of the left particle where the inertial and the non-inertial particles rotate in different directions. This is because the centrifugal acceleration dominates for the inertial particle, and once it gains enough momentum, it continues that direction of rotation

## Slide 25: Conclusions and Future Work
  Optimal-collection path planning
  Implementation in real ocean cases
  Account for cases where the background field is affected by collection
  Account for stochasticity in ocean flow
  Optimal information harvesting and onboard assimilation
  Lagrangian analysis of inertial particles
  Implementation in real ocean cases and inclusion of stochasticity
  Comparison with work on advection of sedimenting plastics
  Assimilation of inertial tracer fields based on tracer observations
Future Work
Conclusions:
  Optimal-collection path planning
  Derived an exact algorithm for time-optimal collection of background field by extending existing methods for time-optimal path planning
  Demonstrated working examples for energy-optimal and optimal-collection path planning
  Lagrangian Analysis of inertial particles
  Derived a PDE to compute the flow map of inertial particles in a fluid flow
  Demonstrated numerical test case using the higher-dimensional flow map
25
Notes: This is more in ‘future work’

## Slide 26: Interpreting the flow map
Like for the case of passive particles, we can use the flow maps to now compute various Lagrangian fields that help us understand how inertial particles are transported
26
Notes: This is more in ‘future work’

## Slide 27
Thank You!
27

## Slide 28
Extra Slides
28

## Slide 29
When characteristics of the hyperbolic PDE intersect, the solution becomes non-differentiable due to formation of shocks
Among all possible weak solutions, viscosity solution picks out the unique solution that satisfies the entropy condition of Sethian
Entropy condition: ‘If the moving level set is a flame front burning unburnt regions, then once a region is burnt, it stays burnt’
Sharp corners arise
even from smooth IC
Sharp IC
Smooth IC
Viscosity Solution
Notes: PL: you still need to fix this
You need to have a section on “extra slides” which you will show if they ask questions on that topic.
And then, have slides that are old in another section after (most likely, you will not show those)

## Slide 30
WENO Scheme
Based on upwinding, but use better approximations for
Use the smoothest polynomial interpolating , and differentiate it (along each dimension)
Decide smoothness by comparing magnitude of the divided differences and choosing the smaller one for each order
End up with 3 possible stencils for :
Use weighted sum of these (weights decided by stencil smoothness)
(similar for )

## Slide 31
Godunov Scheme
Look at as
Use upwinding, but here the velocity is
Looking at the X direction:
Case 1
Case 2
Case 3
Case 4

## Slide 32
Godunov Scheme
Look at as
Use upwinding, but here the velocity is
Looking at the X direction:
Case 1
Case 2
Case 3
Case 4

## Slide 33: Example 3: Energy-Optimal Path Planning, Validation
No flow, no []
Start point
Final point
33

## Slide 34: Example 3: Energy-Optimal Path Planning, Validation
The case
Start point
Final point
34

## Slide 35: Method of Flow Map Composition
Forward flow map
Backward flow map
Forward advection
Backward advection
is an interpolation operator to interpolate the new flow map at locations given by the previous flow map (order of interpolation same as order of advection)
Interpolate and compose to get the flow map
Forward flow map
Backward flow map
Independently compute each constituent flow map
Then
Final equations become:
Kulkarni et al., in prep.
Notes: Once we have these composition equations, then we can use the advection PDE to solve for each of the flow maps
To compute the flow map through composition, initialize a new level set at every timestep and advect it for one timestep.
Note that each of the flow map computation over a time step in independent
We also need to interpolate the values of the new flow map at the values specified by the earlier flow map